## Slide 1: Dr. Taoufik Salem Saidani
CPCS214_CPIT210_CPIS210 Computer Architecture
Lecture# 1
Introduction & Number Systems

## Slide 2: Introduction
Vacuum Tubes

## Slide 3: Introduction
Transistor
Integrated Circuits (IC)

## Slide 4: Introduction
Microprocessor
Computers

## Slide 5: Digital Electronics ……….Everywhere

## Slide 6: Analog and Digital Signal
Analog signals vary continuously over a specified range with infinite values.
t
X(t)
Analog signal
  Digital signals can assume only finite values.
Sampled
Quantized
Digital

## Slide 7: Binary Digital Signal
Digital signals take finite values
  Binary logic (2 values: switch on , switch off)
  Tri-Logic ( 3 values: traffic signal green, red, yellow)
  Quad Logic (4 values: right , left , up, down)
  Two level, or binary values are the most prevalent values.

## Slide 8: Binary Digital Signal
Binary values are represented abstractly by:
  Digits 0 and 1
  Words (symbols) False (F) and True (T)
  Words (symbols) Low (L) and High (H)
  And words On and Off
Binary values are represented by values or ranges of values of physical quantities.
t
V(t)
Binary digital signal
Logic 1
Logic 0
undefined

## Slide 9: Decimal Number System
Base (also called radix) = 10
  10 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Digit Position
  Integer & fraction
Digit Weight
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
5
1
2
7
4
10
1
0.1
100
0.01
500
10
2
0.7
0.04
d2*B2+d1*B1+d0*B0+d-1*B-1+d-2*B-2
(512.74)10

## Slide 10: Binary Number System
Base = 2
  2 digits { 0, 1 }, called binary digits or “bits”
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Bit x Weight”
Formal Notation
Groups of bits
1 binary digit = bit
4bits = Nibble
8 bits = Byte
1
0
-1
2
-2
2
1
1/2
4
1/4
1
0
1
0
1
1 *22+0 *21+1 *20+0 *2-1+1 *2-2
=(5.25)10
(101.01)2
1 0 1 1
1 1 0 0 0 1 0 1

## Slide 11: Octal Number System
Base = 8
  8 digits { 0, 1, 2, 3, 4, 5, 6, 7 }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
8
1
1/8
64
1/64
5
1
2
7
4
5 *82+1 *81+2 *80+7 *8-1+4 *8-2
=(330.9375)10
(512.74)8

## Slide 12: Hexadecimal Number System
Base = 16
  16 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F } Where : A=10, B=11, C=12, D=13, E=14, F=15
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
1
0
-1
2
-2
16
1
1/16
256
1/256
1
E
5
7
A
1 *162+14 *161+5 *160+7 *16-1+10 *16-2
=(485.4765625)10
(1E5.7A)16

## Slide 13: The Power of 2
n | 2n
0 | 20=1
1 | 21=2
2 | 22=4
3 | 23=8
4 | 24=16
5 | 25=32
6 | 26=64
7 | 27=128
n | 2n
8 | 28=256
9 | 29=512
10 | 210=1024
11 | 211=2048
12 | 212=4096
20 | 220=1M
30 | 230=1G
40 | 240=1T
Mega
Giga
Tera
Kilo

## Slide 14: Number Base Conversions
Decimal
(Base 10)
Octal
(Base 8)
Binary
(Base 2)
Hexadecimal
(Base 16)
Evaluate Magnitude
Evaluate Magnitude
Evaluate Magnitude

## Slide 15
Decimal, Binary, Octal and Hexadecimal
Decimal | Binary | Octal | Hex
00 | 0000 | 00 | 0
01 | 0001 | 01 | 1
02 | 0010 | 02 | 2
03 | 0011 | 03 | 3
04 | 0100 | 04 | 4
05 | 0101 | 05 | 5
06 | 0110 | 06 | 6
07 | 0111 | 07 | 7
08 | 1000 | 10 | 8
09 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F
15

## Slide 16: Decimal (Integer) to Binary Conversion
Divide the number by the ‘Base’ (=2)
Take the remainder (either 0 or 1) as a coefficient
Take the quotient and repeat the division
Example: (13)10
Quotient
Remainder
Coefficient
Answer: (13)10 = (a3 a2 a1 a0)2 = (1101)2
MSB LSB
13
/ 2 = 6
1 a0 = 1
6
/ 2 = 3
0 a1 = 0
3
/ 2 = 1
1 a2 = 1
1
/ 2 = 0
1 a3 = 1

## Slide 17: Decimal (Fraction) to Binary Conversion
Multiply the number by the ‘Base’ (=2)
Take the integer (either 0 or 1) as a coefficient
Take the resultant fraction and repeat the division
Example: (0.625)10
Integer
Fraction
Coefficient
Answer: (0.625)10 = (0.a-1 a-2 a-3)2 = (0.101)2
MSB LSB
0.625
* 2 = 1 . 25
0.25
* 2 = 0 . 5 a-2 = 0
0.5
* 2 = 1 . 0 a-3 = 1
a-1 = 1

## Slide 18: Decimal to Octal Conversion
Example: (175)10
Quotient
Remainder
Coefficient
Answer: (175)10 = (a2 a1 a0)8 = (257)8
175
/ 8 = 21
7 a0 = 7
21
/ 8 = 2
5 a1 = 5
2
/ 8 = 0
2 a2 = 2
Example: (0.3125)10
Integer
Fraction
Coefficient
Answer: (0.3125)10 = (0.a-1 a-2 a-3)8 = (0.24)8
0.3125
* 8 = 2 . 5
0.5
* 8 = 4 . 0 a-2 = 4
a-1 = 2

## Slide 19: Binary − Octal Conversion
8 = 23
Each group of 3 bits represents an octal digit
Octal | Binary
0 | 0 0 0
1 | 0 0 1
2 | 0 1 0
3 | 0 1 1
4 | 1 0 0
5 | 1 0 1
6 | 1 1 0
7 | 1 1 1
Example:
( 1 0 1 1 0 . 0 1 )2
( 2 6 . 2 )8
Assume Zeros
Works both ways (Binary to Octal & Octal to Binary)

## Slide 20: Binary − Hexadecimal Conversion
16 = 24
Each group of 4 bits represents a hexadecimal digit
Hex | Binary
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1
A | 1 0 1 0
B | 1 0 1 1
C | 1 1 0 0
D | 1 1 0 1
E | 1 1 1 0
F | 1 1 1 1
Example:
( 1 0 1 1 0 . 0 1 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Binary to Hex & Hex to Binary)

## Slide 21: Octal − Hexadecimal Conversion
Convert to Binary as an intermediate step
Example:
( 0 1 0 1 1 0 . 0 1 0 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Octal to Hex & Hex to Octal)
( 2 6 . 2 )8
Assume Zeros

## Slide 22: Binary Addition
Column Addition
1
0
1
1
1
1
1
1
1
1
0
+
0
0
0
0
1
1
1
= (10)2
1
1
1
1
1
1
= 61
= 23
= 84
carry bit

## Slide 23: Binary Subtraction
Borrow a “Base” when needed
0
0
1
1
1
0
1
1
1
1
0
−
0
1
0
1
1
1
0
= (10)2
2
2
2
2
1
0
0
0
1
= 77
= 23
= 54

## Slide 24: Binary Multiplication
Bit by bit
0
1
1
1
1
0
1
1
0
0
0
0
0
0
0
1
1
1
1
0
1
1
1
1
0
0
0
0
0
0
1
1
0
1
1
1
0
x

## Slide 25: Complements
Diminished Radix Complement - (r-1)’s Complement
  Given a number N in base r having n digits, the (r–1)’s complement of N is defined as:
  (rn –1) – N
Example for 6-digit decimal numbers:
  9’s complement is (rn – 1)–N = (106–1)–N = 999999–N
  9’s complement of 546700 is 999999–546700 = 453299
Example for 7-digit binary numbers:
  1’s complement is (rn – 1) – N = (27–1)–N = 1111111–N
  1’s complement of 1011000 is 1111111–1011000 = 0100111

## Slide 26: Complements
1’s Complement (Diminished Radix Complement)
  All ‘0’s become ‘1’s
  All ‘1’s become ‘0’s
  Example (10110000)2
   (01001111)2
  If you add a number and its 1’s complement …
1 0 1 1 0 0 0 0
+ 0 1 0 0 1 1 1 1
1 1 1 1 1 1 1 1

## Slide 27: Complements
Radix Complement
Example: Base-10
Example: Base-2
The r's complement of an n-digit number N in base r is defined as
rn – N for N ≠ 0 and as 0 for N = 0. Comparing with the (r  1) 's complement, we note that the r's complement is obtained by adding 1 to the (r  1) 's complement, since rn – N = [(rn  1) – N] + 1.
The 10's complement of 012398 is 987602
The 10's complement of 246700 is 753300
The 2's complement of 1101100 is 0010100
The 2's complement of 0110111 is 1001001

## Slide 28: Complements
2’s Complement (Radix Complement)
  Take 1’s complement then add 1 or,
  Toggle all bits to the left of the first ‘1’ from the right
  Example:
  Number:
  1’s Comp.:
0 1 0 1 0 0 0 0
1 0 1 1 0 0 0 0
0 1 0 0 1 1 1 1
+ 1
1 0 1 1 0 0 0 0
0
0
0
0
1
0
1
0

## Slide 29: Complements
Subtraction with Complements
Example
  Using 10's complement, subtract M-N=72532 – 03250.

## Slide 30: Complements
Example
  Using 10's complement, subtract M-N= 03250 – 72532.
There is no end carry.
Therefore, the answer is – (10's complement of 30718) =  69282.

## Slide 31: Complements
Example
  Given the two binary numbers X = 1010100 and Y = 1000011, perform the subtraction (a) X – Y ; and (b) Y  X, by using 2's complement.
There is no end carry. Therefore, the answer is Y – X =  (2's complement of 1101111) =  0010001.

## Slide 32: Dr. Taoufik Salem Saidani
CPCS214_CPIT210_CPIS210: Computer Architecture
Lecture# 1
Signed Binary Numbers

## Slide 33: Signed Binary Numbers
To represent negative integers, we need a notation for negative values (bit placed in the leftmost position).
The convention is to make the sign bit 0 for positive value and 1 for negative value.
Example:

## Slide 34: Signed Binary Numbers
Range for signed
n-bit numbers:
- 2(n-1)  + 2 (n-1) -1

## Slide 35: Signed Binary Numbers
Arithmetic addition (using 2’s complement)
Example: n=8 bit code including sign bit (Range -128  +127)

## Slide 36: Signed Binary Numbers
An overflow condition can be detected by observing the carry into the sign bit position and the carry out of the sign bit position. If these two bits are not equal an overflow or underflow is occurred.

## Slide 37: Signed Binary Numbers
Comment | Carry out of Sign bit | Carry in of Sign bit
Overflow | 0 | 1
Underflow | 1 | 0
Positive results | 0 | 0
Negative results | 1 | 1

## Slide 38: Quiz# 1
Perform the following arithmetic operations using 7-bit signed binary numbers:
+ 51 - 36
+ 23 - 28
ـــــــــ ـــــــــــ